Module 1: Low level Technologies – Further Investigation Questions

Class 1: Introduction
Question: New Computer Technology or Product

UCIe (Universal Chiplet Interconnect Express)
Background
The UCIe standard is open industry standard allowing the connections of different chiplets in a single package. Moors Law, where the prediction of transistor in an IC (Integrated Circuit) doubles every two years, is coming to an end due to physical limits as you can't keep making things smaller forever. Despite this the need for more powerful chips and systems are still growing, thus the next logical step is to make the chips lager to hold more transistors. This idea of just making the chips larger have its own issues, like the low yield from each wafer of silicon as one small defect in the silicon and the entire chip is lost. With chiplets if a defect is found only a small segment is thrown out.

What is UCIe
The UCIe standard is a standardized way to connect chiplets, such as the memory, CPU, graphics, Wi-Fi module and so forth on a single SOC. The ability to have each chiplet responsible for a different task and be connected in a standard way should allow different companies to make different chiplets for different rolls on the same chip. For example, the compute unit chiplets could be made from Intell and the on-board graphics chiplet can come from AMD and so forth with many others. As the UCIe standard allows chiplets to communicate, each chiplet could be developed on a different size process node. Due to Wi-Fi and 5G chips working better on larger process node, this could allow to have these models tightly integrated to the chip without compromising its performance.

NEEDS REFRANCES AND IN TEXT REFRANCES
Class 2: Computer Hardware
Question: Deep Learning Chips

Deep Learning Chips also known as AI chips are designed to accelerate applications that are using artificial neural network (ANN). Some AI chips such as Neuromorphic Processing Units (NPU’s) are chips designed to emulate a human brain to try and help AI models to learn at an accelerated rate and beyond what a normal CPU could do.

Differences between AI chips and Normal Processors
An AI chip is meant to make all AI tasks more effectively and efficiently, where as normal processors are just meant to run any application, it's been given. The AI chips achieves this by having special functions that speed up machine learning tasks, thus normal processers without these functions struggle at AI tasks.

Extreme uses of AI chips
In a paper about Google AI chips published my Cornell University, google researchers used an AI model, dubbed Apollo, to better design most types of chips such as CPU’s, GPU’s and even AI chips. The model uses Architecture from different chip Architectures like x84 and uses this transferable to create chip designs and architectures that have improvements of up to 25%. It's a case of AI creating AI chips to speed up AI.

Class 3: Operating Systems
Question: Mainstream operating system changes
Microsoft and Apple have both created their own Operating Systems. Primarily used today it is Windows 10/11 from Microsoft and for Apple its macOS and iOS. Windows and macOS together have a total market share off over 90% in the desktop sapce

Class 3: Networking
Question: New Networking Technologies

A new product lolol

- Bluetooth	5
  - Frequency	2.4GHz
- 5G
- LoRaWan

[1]